## Slide 1: Assembly Language for x86 Processors
(c) Pearson Education, 2014. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
7th Edition
Kip R. Irvine
Chapter 5: Procedures

## Slide 2: Chapter Overview
Stack Operations
Defining and Using Procedures
Linking to an External Library
The Irvine32 Library
64-Bit Assembly Programming

## Slide 3: Stack Operations
Runtime Stack
PUSH Operation
POP Operation
PUSH and POP Instructions
Using PUSH and POP
Example: Reversing a String
Related Instructions

## Slide 4: Runtime Stack
Imagine a stack of plates . . .
  plates are only added to the top
  plates are only removed from the top
  LIFO structure
10
9
8
7
6
5
4
3
2
1
top
bottom

## Slide 5: Runtime Stack
* SP in Real-address mode
00000006
ESP
00001000
Managed by the CPU, using two registers
  SS (stack segment)
  ESP (stack pointer) *
Offset
00000FFC
00000FF8
00000FF4
00000FF0

## Slide 6: PUSH Operation (1 of 2)
A 32-bit push operation decrements the stack pointer by 4 and copies a value into the location pointed to by the stack pointer.
00000006
ESP
00000FF8
00000FF4
00000FF0
ESP
00001000
BEFORE
00000FFC
00000FF8
00000FF4
00000FF0
AFTER
00001000 00000006
00000FFC 000000A5

## Slide 7: PUSH Operation (2 of 2)
Same stack after pushing two more integers:
00000006
ESP
Offset
00001000
00000FFC
00000FF8
00000FF4
00000FF0
000000A5
00000001
00000002
The stack grows downward. The area below ESP is always available (unless the stack has overflowed).

## Slide 8: POP Operation
Copies value at stack[ESP] into a register or variable.
Adds n to ESP, where n is either 2 or 4.
  value of n depends on the attribute of the operand receiving the data
BEFORE
AFTER
ESP
ESP
00001000 00000006
00000FFC 000000A5
00000FF8 00000001
00000FF4 00000002
00000FF0
00001000 00000006
00000FFC 000000A5
00000FF8 00000001
00000FF4
00000FF0

## Slide 9: PUSH and POP Instructions
PUSH syntax:
  PUSH r/m16
  PUSH r/m32
  PUSH imm32
POP syntax:
  POP r/m16
  POP r/m32

## Slide 10: Using PUSH and POP
push push push | esi ecx ebx | ; | push registers
mov mov mov call | esi,OFFSET dwordVal ecx,LENGTHOF dwordVal ebx,TYPE dwordVal DumpMem | ; | display some memory
pop pop pop | ebx ecx esi | ; | restore registers
Save and restore registers when they contain important values. PUSH and POP instructions occur in the opposite order.

## Slide 11: Example: Nested Loop
mov ecx,100
L1:
push ecx
; set outer loop count
; begin the outer loop
; save outer loop count
mov ecx,20
L2:
; set inner loop count
; begin the inner loop
;
;
loop L2 ; repeat the inner loop
pop ecx loop L1
; restore outer loop count
; repeat the outer loop
When creating a nested loop, push the outer loop counter before entering the inner loop:

## Slide 12: Example: Reversing a String
Use a loop with indexed addressing
Push each character on the stack
Start at the beginning of the string, pop the stack in reverse order, insert each character back into the string
Source code
Q: Why must each character be put in EAX before it is pushed?
Because only word (16-bit) or doubleword (32-bit) values can be pushed on the stack.

## Slide 14: Your turn . . .
Using the String Reverse program as a starting point,
#1: Modify the program so the user can input a string containing between 1 and 50 characters.
#2: Modify the program so it inputs a list of 32-bit integers from the user, and then displays the integers in reverse order.

## Slide 15: Related Instructions
PUSHFD and POPFD
  push and pop the EFLAGS register
PUSHAD pushes the 32-bit general-purpose registers on the stack
  order: EAX, ECX, EDX, EBX, ESP, EBP, ESI, EDI
POPAD pops the same registers off the stack in reverse order
  PUSHA and POPA do the same for 16-bit registers

## Slide 16: Your Turn . . .
Write a program that does the following:
  Assigns integer values to EAX, EBX, ECX, EDX, ESI, and EDI
  Uses PUSHAD to push the general-purpose registers on the stack
  Using a loop, your program should pop each integer from the stack and display it on the screen

## Slide 17: What's Next
Stack Operations
Defining and Using Procedures
Linking to an External Library
The Irvine32 Library
64-Bit Assembly Programming

## Slide 18: Defining and Using Procedures
Creating Procedures
Documenting Procedures
Example: SumOf Procedure
CALL and RET Instructions
Nested Procedure Calls
Local and Global Labels
Procedure Parameters
Flowchart Symbols
USES Operator

## Slide 19: Creating Procedures
Large problems can be divided into smaller tasks to make them more manageable
A procedure is the ASM equivalent of a Java or C++ function
Following is an assembly language procedure named sample:
sample PROC
.
.
ret sample ENDP

## Slide 20: Documenting Procedures
Suggested documentation for each procedure:
A description of all tasks accomplished by the procedure.
Receives: A list of input parameters; state their usage and requirements.
Returns: A description of values returned by the procedure.
Requires: Optional list of requirements called preconditions that must be satisfied before the procedure is called.
If a procedure is called without its preconditions satisfied, it will probably not produce the expected output.

## Slide 21: Example: SumOf Procedure
; SumOf PROC
;
; Calculates and returns the sum of three 32-bit integers.
; Receives: EAX, EBX, ECX, the three integers. May be
; signed or unsigned.
; Returns: EAX = sum, and the status flags (Carry,
; Overflow, etc.) are changed.
; Requires: nothing
; add eax,ebx
add eax,ecx ret
SumOf ENDP

## Slide 22: CALL and RET Instructions
The CALL instruction calls a procedure
  pushes offset of next instruction on the stack
  copies the address of the called procedure into EIP
The RET instruction returns from a procedure
  pops top of stack into EIP

## Slide 23: CALL-RET Example (1 of 2)
main PROC
00000020 call MySub
00000025 mov eax,ebx
.
.
main ENDP
MySub PROC
00000040 mov eax,edx
.
.
ret MySub ENDP
0000025 is the offset of the instruction immediately following the CALL instruction
00000040 is the offset of the first instruction inside MySub

## Slide 24: CALL-RET Example (2 of 2)
00000025
ESP
EIP
00000040
The CALL instruction pushes 00000025 onto the stack, and loads 00000040 into EIP
00000025
ESP
EIP
00000025
The RET instruction pops 00000025 from the stack into EIP
(stack shown before RET executes)

## Slide 25: Nested Procedure Calls
main PROC
.
.
call Sub1 exit
main ENDP
Sub1 PROC
.
.
call Sub2 ret
Sub1 ENDP
Sub2 PROC
.
.
call Sub3 ret
Sub2 ENDP
Sub3 PROC
.
.
ret Sub3 ENDP
(ret to main)
(ret to Sub1) (ret to Sub2)
ESP
By the time Sub3 is called, the stack contains all three return addresses:

## Slide 26: Local and Global Labels
main PROC |  |  | 
jmp L2 | ; | error | 
L1:: | ; | global | label
exit main ENDP
; local label
; ok
sub2 PROC L2:
jmp L1 ret
sub2 ENDP
A local label is visible only to statements inside the same procedure. A global label is visible everywhere.

## Slide 27: Procedure Parameters (1 of 3)
A good procedure might be usable in many different programs
  but not if it refers to specific variable names
Parameters help to make procedures flexible because parameter values can change at runtime

## Slide 28: Procedure Parameters (2 of 3)
mov | esi,0 |  | ; | array index
mov | eax,0 |  | ; | set the sum to zero
mov | ecx,LENGTHOF | myarray | ; | set number of elements
L1: add eax,myArray[esi] add esi,4
loop L1
; add each integer to sum
; point to next integer
; repeat for array size
; store the sum
mov theSum,eax ret
ArraySum ENDP
The ArraySum procedure calculates the sum of an array. It makes two references to specific variable names:
ArraySum PROC
What if you wanted to calculate the sum of two or three arrays within the same program?

## Slide 29: Procedure Parameters (3 of 3)
L1: add eax,[esi] add esi,4 loop L1
; add each integer to sum
; point to next integer
; repeat for array size
ret ArraySum ENDP
This version of ArraySum returns the sum of any doubleword array whose address is in ESI. The sum is returned in EAX:
ArraySum PROC
; Receives: ESI points to an array of doublewords,
; ECX = number of array elements.
; Returns: EAX = sum
; mov eax,0 ; set the sum to zero

## Slide 30: USES Operator
Lists the registers that will be preserved
; set the sum to zero
ArraySum PROC USES esi ecx mov eax,0
etc.
MASM generates the code shown in gold:
ArraySum PROC push esi push ecx
.
.
pop ecx pop esi ret
ArraySum ENDP

## Slide 31: When not to push a register
SumOf PROC | ; | sum of three integers
push eax | ; | 1
add eax,ebx | ; | 2
add eax,ecx | ; | 3
pop eax | ; | 4
ret |  | 
SumOf ENDP
The sum of the three registers is stored in EAX on line (3), but the POP instruction replaces it with the starting value of EAX on line (4):

## Slide 32: What's Next
Stack Operations
Defining and Using Procedures
Linking to an External Library
The Irvine32 Library
64-Bit Assembly Programming

## Slide 33: Linking to an External Library
What is a Link Library?
How the Linker Works

## Slide 34: What is a Link Library?
A file containing procedures that have been compiled into machine code
  constructed from one or more OBJ files
To build a library, . . .
  start with one or more ASM source files
  assemble each into an OBJ file
  create an empty library file (extension .LIB)
  add the OBJ file(s) to the library file, using the Microsoft LIB utility

## Slide 35: How The Linker Works
Your programs link to Irvine32.lib using the linker command inside a batch file named make32.bat.
Notice the two LIB files: Irvine32.lib, and kernel32.lib
  the latter is part of the Microsoft Win32 Software Development Kit (SDK)
kernel32.dll
kernel32.lib | 
exec | utes
Irvine32.lib | 
links | to
Your program |  | links
 |  | to
 | can link to | 

## Slide 36: What's Next
Stack Operations
Defining and Using Procedures
Linking to an External Library
The Irvine32 Library
64-Bit Assembly Programming

## Slide 37: Calling Irvine32 Library Procedures
INCLUDE | Irvine32.inc |  | 
.code |  |  | 
mov | eax,1234h | ; | input argument
call | WriteHex | ; | show hex number
call | Crlf | ; | end of line
Call each procedure using the CALL instruction. Some procedures require input arguments. The INCLUDE directive copies in the procedure prototypes (declarations).
The following example displays "1234" on the console:

## Slide 38: Library Procedures - Overview (1 of 4)
CloseFile – Closes an open disk file
Clrscr - Clears console, locates cursor at upper left corner CreateOutputFile - Creates new disk file for writing in output mode Crlf - Writes end of line sequence to standard output
Delay - Pauses program execution for n millisecond interval DumpMem - Writes block of memory to standard output in hex
DumpRegs – Displays general-purpose registers and flags (hex) GetCommandtail - Copies command-line args into array of bytes GetDateTime – Gets the current date and time from the system GetMaxXY - Gets number of cols, rows in console window buffer GetMseconds - Returns milliseconds elapsed since midnight

## Slide 39: Library Procedures - Overview (2 of 4)
GetTextColor - Returns active foreground and background text colors in the console window
Gotoxy - Locates cursor at row and column on the console
IsDigit - Sets Zero flag if AL contains ASCII code for decimal digit (0–9) MsgBox, MsgBoxAsk – Display popup message boxes
OpenInputFile – Opens existing file for input ParseDecimal32 – Converts unsigned integer string to binary ParseInteger32 - Converts signed integer string to binary
Random32 - Generates 32-bit pseudorandom integer in the range 0 to FFFFFFFFh
Randomize - Seeds the random number generator
RandomRange - Generates a pseudorandom integer within a specified range
ReadChar - Reads a single character from standard input

## Slide 40: Library Procedures - Overview (3 of 4)
ReadDec - Reads 32-bit unsigned decimal integer from keyboard ReadFromFile – Reads input disk file into buffer
ReadHex - Reads 32-bit hexadecimal integer from keyboard ReadInt - Reads 32-bit signed decimal integer from keyboard ReadKey – Reads character from keyboard input buffer
ReadString - Reads string from stdin, terminated by [Enter]
SetTextColor - Sets foreground/background colors of all subsequent text output to the console
Str_compare – Compares two strings
Str_copy – Copies a source string to a destination string Str_length – Returns the length of a string in EAX Str_trim - Removes unwanted characters from a string.

## Slide 41: Library Procedures - Overview (4 of 4)
Str_ucase - Converts a string to uppercase letters.
WaitMsg - Displays message, waits for Enter key to be pressed WriteBin - Writes unsigned 32-bit integer in ASCII binary format. WriteBinB – Writes binary integer in byte, word, or doubleword format WriteChar - Writes a single character to standard output
WriteDec - Writes unsigned 32-bit integer in decimal format WriteHex - Writes an unsigned 32-bit integer in hexadecimal format
WriteHexB – Writes byte, word, or doubleword in hexadecimal format WriteInt - Writes signed 32-bit integer in decimal format

## Slide 42: Library Procedures - Overview (5 of 4)
WriteStackFrame - Writes the current procedure’s stack frame to the console.
WriteStackFrameName - Writes the current procedure’s name and stack frame to the console.
WriteString - Writes null-terminated string to console window WriteToFile - Writes buffer to output file
WriteWindowsMsg - Displays most recent error message generated by MS-Windows

## Slide 43: Example 1
Clear the screen, delay the program for 500 milliseconds, and dump the registers and flags.
.code
call Clrscr mov eax,500 call Delay call DumpRegs
Sample output:
EAX=00000613 EBX=00000000 ECX=000000FF EDX=00000000 ESI=00000000 EDI=00000100 EBP=0000091E ESP=000000F6 EIP=00401026 EFL=00000286 CF=0 SF=1 ZF=0 OF=0

## Slide 44: Example 2
Display a null-terminated string and move the cursor to the beginning of the next screen line.
.data
str1 BYTE "Assembly language is easy!",0
.code
mov edx,OFFSET str1 call WriteString call Crlf

## Slide 45: Example 2a
Display a null-terminated string and move the cursor to the beginning of the next screen line (use embedded CR/LF)
.data
str1 BYTE "Assembly language is easy!",0Dh,0Ah,0
.code
mov edx,OFFSET str1 call WriteString

## Slide 46: Example 3
mov | eax,IntVal |  |  | 
call | WriteBin | ; | display | binary
call | Crlf |  |  | 
call | WriteDec | ; | display | decimal
call | Crlf |  |  | 
call | WriteHex | ; | display | hexadecimal
call | Crlf |  |  | 
Display an unsigned integer in binary, decimal, and hexadecimal, each on a separate line.
IntVal = 35
.code
0000 0000 0000 0000 0000 0000 0010 0011
35
23
Sample output:

## Slide 47: Example 4
Input a string from the user. EDX points to the string and ECX specifies the maximum number of characters the user is permitted to enter.
.data
fileName BYTE 80 DUP(0)
.code
mov edx,OFFSET fileName
mov ecx,SIZEOF fileName – 1 call ReadString
A null byte is automatically appended to the string.

## Slide 48: Example 5
.code
mov ecx,10
; loop counter
L1: mov | eax,100 | ; | ceiling value
call | RandomRange | ; | generate random int
call | WriteInt | ; | display signed int
call | Crlf | ; | goto next display line
loop | L1 | ; | repeat loop
Generate and display ten pseudorandom signed integers in the range 0 – 99. Pass each integer to WriteInt in EAX and display it on a separate line.

## Slide 49: Example 6
Display a null-terminated string with yellow characters on a blue background.
.data
str1 BYTE "Color output is easy!",0
.code
mov eax,yellow + (blue * 16) call SetTextColor
mov edx,OFFSET str1 call WriteString call Crlf
The background color is multiplied by 16 before being added to the foreground color.

## Slide 50: What's Next
Stack Operations
Defining and Using Procedures
Linking to an External Library
The Irvine32 Library
64-Bit Assembly Programming

## Slide 51: 64-Bit Assembly Programming
The Irvine64 Library
Calling 64-Bit Subroutines
The x64 Calling Convention

## Slide 52: The Irvine64 Library
Crlf: Writes an end-of-line sequence to the console.
Random64: Generates a 64-bit pseudorandom integer.
Randomize: Seeds the random number generator with a unique value.
ReadInt64: Reads a 64-bit signed integer from the keyboard.
ReadString: Reads a string from the keyboard.
Str_compare: Compares two strings in the same way as the CMP instruction.
Str_copy: Copies a source string to a target location.
Str_length: Returns the length of a null-terminated string in RAX.
WriteInt64: Displays the contents in the RAX register as a 64-bit signed decimal integer.

## Slide 53: The Irvine64 Library (cont'd)
WriteHex64: Displays the contents of the RAX register as a 64- bit hexadecimal integer.
WriteHexB: Displays the contents of the RAX register as an 8-bit hexadecimal integer .
WriteString: Displays a null-terminated ASCII string.

## Slide 54: Calling 64-Bit Subroutines
Place the first four parameters in registers
Add PROTO directives at the top of your program
  examples:
ExitProcess PROTO WriteHex64 PROTO
; located in the Windows API
; located in the Irvine64 library

## Slide 55: The x64 Calling Convention
Must use this with the 64-bit Windows API
CALl instruction subtracts 8 from RSP
First four parameters must be placed in RCX, RDX, R8, and R9
Caller must allocate at least 32 bytes of shadow space on the stack
When calling a subroutine, the stack pointer must be aligned on a 16-byte boundary.
See the CallProc_64.asm example program.

## Slide 56: Summary
Procedure – named block of executable code
Runtime stack – LIFO structure
  holds return addresses, parameters, local variables
  PUSH – add value to stack
  POP – remove value from stack
Use the Irvine32 library for all standard I/O and data conversion
  Want to learn more? Study the library source code in the c:\Irvine\Examples\Lib32 folder

## Slide 57
55 64 67 61 6E 67 65 6E